深圳市智博电子有限公司               文件编号 Drawing No.：

产 品 规 格 书                 当前版本 Ver： V1.0

# 标题 Title：石英晶体谐振器规格书

石英晶体谐振器

SPECIFICATION FOR QUARTZ CRYSTAL RESONATOR

外  型 Holder Type： SMD-3225

频  率 Frequency：  12.000MHz

| 承认日期 Date of Approval | 年 月 日 Year Month Day |
| --- | --- |
| 承认栏 Approval By |  |

ACCEPTED/CONFIRMED BY（承  认）：

| 设计： Issued by |  | 审核： Checked by |  | 批准： Approved by |  |
| --- | --- | --- | --- | --- | --- |

深圳市智博电子有限公司

SHENZHEN  ZHIBO  ELECTRONICS CO.,LTD..

石英晶体谐振器规格书

# QUARTZ CRYSTAL SPECIFICATION

编 号 Spec No.：                                                  日 期 Date：2009-05

一、适用Scope ：本规格书适用于SMD-3.2*2.5 12.000MHz 晶体谐振器。

This specification is applied to the quartz crystal  SMD-5032  6.000MHz

二、技术指标 Electrical Characteristics

|  | 项目 Item | 规格 Specification |
| --- | --- | --- |
| 1 | 标称频率 Nominal Frequency | 12.000MHz |
| 2 | 壳 形 Holder Type | SMD-3225 |
| 3 | 振动模式 Oscillator Mode | 基频 |
| 4 | 调整频差(25℃) Frequency Stability (25℃) | ±20ppm |
| 5 | 工作温度范围 Operating Temperature Range | -10℃~+70℃ |
| 6 | 温度频差 Frequency Stability vs. Temp | ±30ppm |
| 7 | 负载电容 Load Capacitance | 20pF |
| 8 | 谐振电阻 Equivalent Series Resistance | 40Ω max |
| 9 | 静 电 容 Shunt Capacitance | 7.0pF max |
| 10 | 激励功率 Drive Level | 50μW in standard |
| 11 | 绝缘电阻 Insulation Resistance | 500MΩ at DC100V |
| 12 | 年老化率 Aging Rate a Year | ±3ppm |
| 13 | 检测仪器 Test Impedance Meter | S&A250B |
| 14 | 印字形式 Marking |  |
| 15 | 存储温度范围 Storage Temperature Range | -40℃~+85℃ |
| 16 | 存储湿度范围 Storage Humidity Range | 0～95％ RH |

三、外形及尺寸 Appearance and Dimensions

1. 外观：标志清晰，外表光洁无污点和损伤。

Appearance：Marking clear, no visible damage and dirt.

2. 外形尺寸：图一所示。

Dimensions：See figure 1.

深圳市智博电子有限公司

SHENZHENZHIBO ELECTRONICS CO.,LTD..

石英晶体谐振器规格书

# QUARTZ CRYSTAL SPECIFICATION

编 号 Spec No.：                                                   日 期 Date：2009-03

图一：外形尺寸图   unit：mm

Figure 1. Dimensions

| 序号 | 类 别 | 规 范 | 检验标准 |
| --- | --- | --- | --- |
| 1 | 自由跌落 | 从100cm高度自由跌落到30mm厚硬木板上，跌落三次 | 满足电器性能规定 |
| 2 | 振动 | 频率10~55Hz，振幅1.5mm，X、Y、Z方向各振动2小时。 | 满足电器性能规定 |
| 3 | 引出端强度 | a.拉力：固定振荡器主体，沿引脚轴向施加0.9Kg拉力，保持30±5秒。 b.弯曲：引脚端头悬挂450g的重物，弯曲90°,时间2~3秒，以相同速度返回原位置，再反向操作一次。 | 引脚无拔出或断裂现象 |
| 4 | 密封性 | 将谐振器浸在酒精中，加压5Kg/cm2，时间五分钟。 | 测量引脚与基座间绝缘电阻>500MΩ（DC100V） |
| 5 | 可焊性 | 从引脚末端至底部2~2.5mm放入235℃ ±5℃的焊槽内, 时间2±0.5秒。 | 沾锡面>90%，频率变化≤±10ppm |
| 6 | 耐焊接热 | 从引脚末端至底部2~2.5mm处放入260℃±10℃的焊槽内，时间10±0.5秒 | 外观无异常，满足电器性能规定 |
| 7 | 温度循环 | 将谐振器放置在高低温箱中，将温度设置在-10℃，温度到达后保持30分钟，再将温箱升温到+70℃，保持30分钟，这是一个循环；再将温箱降温到-10℃，开始下一个循环，如此循环三次 | 外观无损伤，满足电器性能规定 |
| 8 | 恒定湿热 | 在40±3℃， 90～95% RH，放置96小时，取出后恢复2小时 | 外观无异常，满足电器性能规定 |
| 9 | 高温老化 | 85℃±2℃老化96小时，取出后常温下恢复2小时 | 外观无异常，满足电器性能规定 |
| 10 | 耐低温 | -40℃±2℃放置96小时，取出后常温下恢复2小时 | 外观无异常，满足电器性能规定 |

四、机械及环境性

四、Physical and Environment Characteristics

| Item | Condition of test | Performance Requirements |
| --- | --- | --- |
| Mechanical Shock | Resonator shall be measured after 3 times random dropping from the height of 100cm onto hard wooden broad of thickness more than 30mm | No visible damage, and measured Values shall meet Table 1 |
| Vibration | Subject resonator to following vibration: Frequency:：10～55Hz Amplitude：1.5mm Duration：3 mutually perpendicular planes in each 2 hours Direction：X Y and Z axis | No visible damage, and measured Values shall meet Table 1 |
| Terminal Strength Terminal Pulling Terminal Bending | Force of 5N is applied to each lead in axial direction for 30±5 sec. When force of 5N is applied to each lead in axial direction, the lead shall folded up 90o from the axial direction and folded back to the axial direction. The speed of folding shall be each 3 seconds. | No visible damage, and measured Values shall meet Table 1 |
| Solder ability | Lead terminals are immersed up to 2mm from Resonator’s body in soldering bath of 235±5℃ for 2±0.5 sec. | More than 90％ of the terminal surface of the resonator shall be covered with fresh solder |
| Resistance to Soldering Heat | Lead terminals are immersed up to 2mm from Resonator’s body in soldering bath of 260±10℃ for 10±0.5 seconds and then resonator shall be measured after being placed in natural conditions for 2 hours. | No visible damage, and measured Values shall meet Table 1 |
| Temperature Cycling | Subject the resonator to -10℃ for 30 min, followed by a high temperature of +70℃ for 30 min. Cycling shall be repeated 5 times. resonator shall be measured after being placed in natural conditions for 2 hours. | No visible damage, and measured Values shall meet Table 1 |
| Heat Resistance | Subject the resonator to +85℃±2℃ for 96 hours, resonator shall be measured after being placed in natural conditions for 2 hours. | No visible damage, and measured Values shall meet Table 1 |
| Cold Resistance | Subject the resonator to -40℃±2℃ for 96 hours, resonator shall be measured after being placed in natural conditions for 2 hours. | No visible damage, and measured Values shall meet Table 1 |
| Humidity | Subject the resonator at +40℃±3℃ and 90％～95％ R.H. for 96 hours, resonator shall be measured after being placed in natural conditions for 2 hours. | No visible damage, and measured Values shall meet Table 1 |